## Slide 1: A novel modeling to generate alternatives approach
Determining the convex hull containing all near optimal solutions
Author: Tim Pedersen
Supervisor: Gorm B. Andresen
Notes: Which means that I have developed a new modeling to generate alternatives approach that I have used to addressing structural uncertainty in energy system models

## Slide 2: Agenda
  Motivation
  Modelling to generate alternatives
  Optimization model
  Experiment results
  Conclusion

## Slide 3: Motivation
  Irreversible climate change
  Large share of emissions are from energy production [1]
  Wind/Solar implementation
  Better models
https://www.eea.europa.eu/data-and-maps/daviz/ghg-emissions-by-aggregated-sector-2#tab-dashboard-01
Chart: CO2 emission by sector 2015
| Energy | Transport | Industry | Residential/comercial | Biomass | Agriculture | Aviation | Waste | Shipping
CO2 emission by sector | 1331272 | 905888 | 857340 | 551616 | 534199 | 515550 | 142182 | 139313 | 134806
[1] European Environment Agency. Annual European union greenhouse gas inventory 1990 – 2015 and inventory report 2017. 2017.
Notes: Pointe: Climate change = need for models

## Slide 4: Motivation - model
Variables:
Constraints:
Feasible decision space:
Convex optimization
Model objective – minimize cost:
Optimal solution
Notes: Pointe: Rough explanation of model

## Slide 5: Motivation - model flaws
  Parametric uncertainty
    Change in weather patterns
    Change in energy demand
    Unknown technology prices
  Structural uncertainty
    Unmodeled objectives
    Political decisions
    Mathematical simplifications
  The true solution is just as likely to be located in the near-optimal regions of the decision space. [2]
[2] Lewis D. Hopkins E. Downey Brill Jr., Shoou-Yuh Changt. Modeling to generate alternatives: The hsj approach and an illustration using aproblem in land use planning. Management Science, 28, 31982.
Notes: Pointe: Structural uncertainty = analyze near optimal region

## Slide 6: Objective
Define a method capable of addressing structural uncertainty in techno-economic models, based on the principles of modeling to generate alternatives (MGA).

## Slide 7: Modeling to generate alternatives
  Method to find alternative near optimal feasible solutions
  MGA constraint:
  New objective function
MGA slack
Near optimal
Feasible space
Minimize
Notes: Pointe: Finite number of points define the entire set

## Slide 8: Modeling to generate alternatives
Existing MGA methods
  Hop Skip Jump (HSJ) [2]
    Minimize all non zero variables
  Random search
  Maximize/Minimize [3]
  Genetic algorithms [4]
Common feature:
  Finite number of solutions
[2] E. Downey Brill Jr., Shoou-Yuh Changt, Lewis D. Hopkins . Modeling to generate alternatives: The hsj approach and an illustration using a problem in land use planning. Management Science, 28, 1982.
[3] Fabian Neumann and Tom Brown. The near-optimal feasible space of a renewable power system model, 2019
[4] Daniel H. Loughlin, S. Ranji Ranjithan, E. Downey Brill JR., and John W. Baugh JR. Genetic algorithm approaches for addressing unmodeled objectives in optimization problems. Engineering Optimization, 2001.

## Slide 9: Novel MGA approach
Regular Optimization
Add MGA constraint
Maximize and minimize all variables
Compute the convex hull and determine face normal directions
Notes: Pointe: Explain novel method

## Slide 10: Novel MGA approach
Optimize using face normal directions to determine the objective function
Repeat step 3
(Compute convex hull and determine face normal directions)
Repeat step 4
Terminate algorithm when iteration criterion is reached
Notes: Pointe: Novel method converges towards full solution + can be expanded to n dimensions

## Slide 11: Modeling to generate alternatives
  Assuming even distribution
  Random sampling across the near optimal feasible space.
  Enough points = Full solution
  Statistics about all feasible solutions
Notes: Pointe: Sampling to gain statistical data about ALL solutions

## Slide 12: Model
  Electricity grid of 30 European countries [5]
  Variables:
    Generator capacities (Wind, Solar, Gas)
    Transmission line capacities
    Hourly energy production
    Hourly energy transmission
  Constants:
    Demand
    Capacity factors
    Technology cost
[5] D.P. Schlachtberger, T. Brown, S. Schramm, and M. Greiner. The benefits of cooperation in a highly renewable european electricity network. Energy, 134:469– 481, 2017.
Notes: Pointe: Model serves as a framework to establish usefulness of the developed method
Simplified by reducing number of technologies

## Slide 13: Model – Reducing Dimensions
Neglecting hourly energy dispatch
Grouping variables by technology
d ≈700.000
d ≈ 90
d ≈ 3-10
Notes: Pointe: Too many dimensions – Reduction methdod

## Slide 14: Model - Multiplicity
  Reducing dimensions = Reducing information
  Full decision space:
    1 Point = 1 solution
  Reduced decision space:
    1 Point = Range of solutions
Notes: Pointe: Assumption about equal distribution doesn't hold

## Slide 15: Experiment
  Euro-30 model
  PyPSA [6]
  PRIME cluster computer
  Parallel processing
  4 Variables (Wind, Solar, Gas, Transmission)
  7 Variables (Capacities North Europe, Capacities South Europe, Transmission)
[6] Tom Brown, Jonas Horsch, and David Schlachtberger. Python for power system analysis (pypsa) version 0.14.1. https://doi.org/10.5281/zenodo.3233682, may 2019

## Slide 16: Results - Optimal solutions
CO2 reduction levels:
0, 50, 80, 95% reduction
Notes: Pointe: Model performs as expected

## Slide 17: Results - MGA
  4 Variables:
    Wind, Solar, Gas (OCGT), Transmission
  10% MGA slack
  Large variance
Notes: Pointe: Large variance

## Slide 18: Results - MGA
  Equality in energy production
  Desire to be self-sufficient
  Gini coefficient
Notes: Pointe: Equality is expensive

## Slide 19: conclusion
  Method successfully developed
  Converges towards full solution
  Quantifies all near optimal solutions
  Method capable of handling 7+ variables
  Great variance in near optimal solutions at small variation in cost
  Method can be used on any linear problem with large structural uncertainty

## Slide 21: Discussion
Comparison of MGA methods
Limitations max 10 dim

## Slide 22: Model - constants
Average capacity factor
Summed electricity demand

## Slide 23: Decision space
Variables:
Decision space:
Constraints:
Feasible decision space:
Notes: Pointe: Explain feasible space in n dimensions

## Slide 24: Model
  Minimize cost
  Linear Constraints
  Optimization
    Simplex method
    Barrier method
Notes: Pointe: Model is linear

## Slide 25: Model - constraints
  Variables:
  Power balance
  Production limitations
  Transmission limitations
  Capacity limitations
  CO2 constraint
Notes: Linear

## Slide 26: Summary
  Model
    Linear constraints
    Data
    Parametric and structural uncertainty
    “True” solution located in inferior region
  MGA method
    Reducing dimensions
    Finds all near optimal feasible solutions
  Results
    Large variance

## Slide 27: Conclusion
A novel modeling to generate alternatives approach has successfully been developed
The method determines the convex hull containing all near optimal solutions